1. Creating a network namespace -
  sudo ip netns add red
2. display network namespaces -
  ip netns list
3. create the veth pair: -
  ip link add veth0 type veth peer name veth1
4. display link -
  ip link list
  ip netns exec blue ip link list
5. connecting Ethernet to namespace
  ip link set veth1 netns blue
6. config ip -
  ip netns exec blue ifconfig veth1 10.1.1.1/24
7. diplay address-
  ip addr list
  ip netns exec blue ip addr list
  ip route list(routiing table)

### Containers and virtual machines have similar resource isolation and allocation benefits, but function differently because containers virtualize the operating system instead of hardware. Containers are more portable and efficient

https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=3&cad=rja&uact=8&ved=2ahUKEwjrlaXSmrTlAhVReH0KHfJvDZ0QFjACegQIDBAJ&url=https%3A%2F%2Fcumulusnetworks.com%2Fblog%2Fwhat-is-container-networking%2F&usg=AOvVaw1Ok6TQ2gTCAkQX_FCkKVQf

containers are a modern application sandboxing mechanism
#### CONTAINERS

The Wikipedia’s definition says “containers is a generic term for an operating system level virtualization. … There are a number of such implementations including Docker, lxc, and rkt.”

In the Unix/Linux System Admin book they describe a container to be an isolated group of processes that are restricted to a private root filesystem and process namespace.

group of processes with some cool kernel feature ,that allow the processes to pretend that they’re running on their own separate machine. While the host machine knows that the container is actually a process, the container thinks that it is a separate machine. These awesome kernel features that make this possible are:
namespaces = Namespaces are the feature that make the container look and feel like it is an entirely separate machine.

https://medium.com/@jessgreb01/what-is-the-difference-between-a-process-a-container-and-a-vm-f36ba0f8a8f7

A container is an isolated execution environment on a Linux host that behaves much like a full-featured Linux installation with its own users, file system, processes and network stack
Running an application inside of a container isolates it from the host and other containers,
meaning that even when the applications inside of them are running as root, they can not access or modify the files, processes, users, or other resources of the host or other containers.

Containers are implemented in the Linux kernel, which means that they share
their resources with their host.
For example, whenever an application is run in a container, it is possible to see the container process in the host operating system’s process table. There is a mapping of “real” user and process ID’s to “fake” process IDs, handled transparently by the kernel.
#### VIRTUAL MACHINES
Virtual machines (VMs) are an abstraction of physical hardware turning one server into many servers. The hypervisor allows multiple VMs to run on a single machine. Each VM includes a full copy of an operating system, the application, necessary binaries and libraries - taking up tens of GBs. VMs can also be slow to boot.
Virtual machines, however, fully simulate all of the hardware of a computer including the peripherals, network adapters, hard drives, memory and CPU instructions. There is much more overhead involved in virtualization, meaning that on average, VMs are larger and slower than their container counterparts. They are also more opaque: applications that run in a VM are not visible in the host operating system’s process table — special hooks into the VM are needed to get that level of visibility.

What is the difference between a container and a virtual machine?

The container’s system requires an underlying operating system that provides the basic services to all of the containerized applications using virtual-memory support for isolation. A hypervisor, on the other hand, runs VMs that have their own operating system using hardware VM support. Container systems have a lower overhead than VMs and container systems typically target environments where thousands of containers are in play. Container systems usually provide service isolation between containers. As a result, container services such as file systems or network support can have limited resource access.

What is the difference between a hub, a switch and a router?

network namespace
       A network namespace is logically another copy of the network stack with its own routes, firewall rules, and network devices.

## Hubs
A hub is the least expensive, least intelligent, and least complicated of the three. Its job is very simple: anything that comes in one port is sent out to the others
## Switches
A switch does what a hub does, but more efficiently. By paying attention to the traffic that comes across it, it learns which computers are connected to which port.

 router

The main objective of router is to connect various networks simultaneously and it works in network layer, whereas the main

objective of switch is to connect various devices simultaneously and it works in data link layer.

Router is compatible with NAT.	While it is not compatible with NAT.

Linux Bridge

A bridge is a device that separates two or more network segments within one logical network (e.g. a single IP-subnet).

Using a Linux Bridge. ... A network bridge is a Link Layer device which forwards traffic between networks based on MAC addresses and is therefore also referred to as a Layer 2 device. It makes forwarding decisions based on tables of MAC addresses which it builds by learning what hosts are connected to each network.

What is Open vSwitch?

http://docs.openvswitch.org/en/latest/faq/general/

A: Open vSwitch is a production quality open source software switch designed to be used as a vswitch in virtualized server environments. A vswitch forwards traffic between different VMs on the same physical host and also forwards traffic between VMs and the physical network.

The role of this software is to forward traffic between different virtual machines (VM) within the same host and even traffic between a VM and a physical network.

## VETH
The VETH (virtual Ethernet) device is a local Ethernet tunnel. Devices are created in pairs, as shown in the diagram below.
Packets transmitted on one device in the pair are immediately received on the other device. When either device is down, the link state of the pair is down.

## Veth Pairs
Veth devices are built as pairs of connected virtual ethernet interfaces[2] and can be thought of as a virtual patch cable. What goes in one end will come out the other.

route

In general, a route refers to the path a data packet travels on a network. The route includes every device that handles the packet between its source to its destination, including routers, switches, and firewalls.

Routing table

In computer networking a routing table, or routing information base, is a data table stored in a router or a network host that lists the routes to particular network destinations, and in some cases, metrics associated with those routes.

What is a route in networking?

Routing is the process of moving a packet of data from one network to another network based on the destination IP address. ... Routers use the information contained in a route to make decisions about which network interface to forward a packet through in order to reach the destination address in the packet

 What is traffic shaping?

Traffic shaping is a bandwidth management technique used on computer networks which delays some or all datagrams to bring them into compliance with a desired traffic profile.[1][2] Traffic shaping is used to optimize or guarantee performance, improve latency, or increase usable bandwidth for some kinds of
packets by delaying other kinds

he practice involves delaying the flow of packets that have been designated as less important or less desired than those of prioritized traffic streams

Time-sensitive data may be given priority over traffic that can be delayed briefly with little-to-no ill effect.

traffic policing

In communications, traffic policing is the process of monitoring network traffic for compliance with a traffic contract and taking steps to enforce that contract.

https://networklessons.com/quality-of-service/qos-traffic-shaping-explained

When we use shaping we will buffer the traffic to a certain bitrate,
policing will drop the traffic when it exceeds a certain bitrate

Your ISP sold you a fibre connection with a traffic contract and a guaranteed bandwidth of 10 Mbit, the fibre interface however is capable of sending 100 Mbit per second. Most ISPs will configure policing to drop all traffic above 10 Mbit so that you can’t get more bandwidth than what you are paying for. It’s also possible that they shape it down to 10 Mbit but shaping means they have to buffer data while policing means they can just throw it away.

Instead of waiting for the policer of the ISP to drop your traffic, you might want to shape your outgoing traffic towards the ISP so that they don’t drop it

## 4.1. qdisc
Simply put, a qdisc is a scheduler (Section 3.2). Every output interface needs a scheduler of some kind, and the default scheduler is a FIFO. Other qdiscs available under Linux will rearrange the packets entering the scheduler's queue in accordance with that scheduler's rules.